## Slide 1: PLC for Home Automation and How to Make It a Honeypot
Philippe Lin (@miaoski)
For BSidesLV 2016
* Special thanks to Ming-Wei Cheng for his PLC-enabled house.
* Thanks Scott Erven for being my mentor 

## Slide 2: Home Automation
https://hackaday.io/post/4337
Notes: Eric Tsai, Wireless home automation with OpenHAB
Awesome design, $20 arduino + Raspberry Pi + RF69M

## Slide 3: PLC for Reliability
Robust – 20 years
Install and forget
IFTTT and HMI (optional)
Notes: Reliability, maintenance cost
Work in the sands

## Slide 4: IFTTT
Notes: Equivalent to Arduino progs, just simpler
My friend’s house

## Slide 5: As You Enter the House ...
Infrared Sensor
Notes: IR  Remote controller to unlock keyless system

## Slide 6: As You Enter the House ...
Rolling code Remote Controller
Notes: Prevents replay attack – Common PRNG and compares within next 256 codes (Wikipedia)

## Slide 7: As You Enter the House ...
Reed Switch

## Slide 8: > 100 dB Siren Buzzes, When ...
You passed the IR sensor, but failed to unlock rolling code controller within 1 min.
Reed switches on doors and windows turn on.
Any circuit got cut
Moreover ...

## Slide 9: UPS and Double-Loop
16 DI
24V
RS485
Alarm
ModBus/TCP
GPRS
12V
Backup Power
DI from reed switches
Omron relays
Notes: ICP DAS

## Slide 10: Heater and Backup Alarm
RS485
GSM Alarm
Sends SMS when PLC is broken, DoS, etc.
Turn on the boiler
before he drives home
Monitors PLC’s heart beat
Notes: GSM Alarm – When PLC malfunctions

## Slide 11: Peripherals
Solenoid Valve
Leak Detector
Gas Sensor
Patrol Helicopter

## Slide 12: Wiring
ICP DAS Wise-5801
DO 0 Relay 1
DO 1 Relay 2
DO 2 Relay 3
DO 3 Relay 4
DO 4 x
DO 5 x
DO 6 x
DO 7 x
DI 0 IR Sensor
DI 1 Key lock
DI 2 Reed 1
DI 3 Reed 2
DI 4 x
DI 5 Reed 3
DI 6 Reed 4
DI 7 Reed 5
RS485 ICP CON
Email + SMS
24V DC + 12V DC Backup
ICP Con i7041PD
IN 0 Reed 6
IN 1 Reed 7
IN 2 Reed 8
IN 3 x
IN 4 x
IN 5 Reed 9
IN 6 Reed 10
IN 7 Reed 11
IN 8 Gas sensor
IN 9 Water leak
IN 10 x
IN 11 x
IN 12 x
IN 13 Reed 12
RS485 ICP DAS
Heater
Omron Relays
#1 Alarm (NC)
#2 Out
#3 Heater
#4 Alarm (NC)
#5 ATS
Sancue Heater
Power
RS485
Resets GSM Alarm
Backup power for peripherals
Notes: IN => Pulled high when closed, LOW = trigger

## Slide 13: How to Break Into the House?
Trigger IR Sensor without key lock  Bam!
Open door / windows without key unlock  Bam!
Cut off AC power  UPS backup
Short circuit because it’s low triggered  Maybe
Hack into VPN  Maybe
  Send a phishing email to get IP address
  Asus home router vulnerability
  Stop countdown timer
  Change ModBus settings
  DoS PLC
Sends email when door is opened
Buzz when PLC resets
SMS when PLC stops heartbeat
Notes: No glass vibration alarm

## Slide 14: How to Break Into the House?
UPS power-rail fails
  Backup UPS power-rail fails, too.
Smash and grab!
  Few more minutes to cut the wire mesh glass.
Break the PRNG in rolling code
  Replay attack  Samy Kamkar in DEFCON23.
Use acetylene cutter
Murphy’s law!
Anything that can go wrong, will go wrong.
Notes: Thieves might want to choose another house (mesh glass)

## Slide 15
So, what’s next, if the house is robust?

## Slide 16: 1-Level Honeypot
Discrete input = Window open / close
Coils = Lamps or water faucets
Input registers = temperature, humidity
Holding registers = target temperature
Add some camouflage and make it look like some industry?
https://www.trendmicro.com/vinfo/us/security/news/
cybercrime-and-digital-threats/the-gaspot-experiment
Notes: After having a super secure house, we make it a source of hour honeypot

## Slide 17: 1-Level Honeypot Architecture
PLC at Home
ModBus TCP/502
HMI written in Python
(Exposed)
Intermediate ModBus
(Exposed)
K wants to
change the coils
K browses the HMI and feels happy
Copy the readings every t seconds
Display on
Log the changes
It’s not very interesting to simply copy the readings, though.
Notes: Smith K, check Franz Kafka.

## Slide 18: 2-Level Honeypot
Self-adaptive honeypot (?)
States change in a predefined way, yet readings will match PLC@home.
  Procrastinated
  Incremental
  Change in a given rate
Can deploy multiple honeypots and change fuzzy factors (ransom seeds, changing rate)
How about binding a pseudo-pump?

## Slide 19: 2-Level Honeypot Architecture
PLC at Home
ModBus TCP/502
HMI written in Python
(read only)
Intermediate ModBus
exposed on Internet
K wants to
change the coils
K browses the HMI and feels happy
Fuzzily matches the readings to
Display on
Log the changes
Notes: Smith K, of course

## Slide 20
Ground Truth (PLC)
1-Level Honeypot
2-Level Honeypot
Heart beat pin
If someone sets CO#8 and CO#10
Delayed

## Slide 21
Ground Truth (PLC)
1-Level Honeypot
2-Level Honeypot
Scaled fallback to ground truth

## Slide 22: Simulate a Pump
DI#7
DI#6
CO#6
Increases until DI#7 goes low
Notes: In 20 lines of Python

## Slide 23: Recap
PLC with double loop for robust home security.
Simple honeypot that copies from PLC.
Adaptive honeypot that copies from PLC.
Simulate a pump or other circuits based on PLC.
Codes and materials: https://github.com/miaoski/bsideslv-plc-home
Notes: Thanks Scott again

## Slide 24: Question / Demo philippe_z_lin@trendmicro.com @miaoski Code in https://github.com/miaoski/bsideslv-plc-home